## Slide 1: Traffic Matrix Prediction based on Bidirectional Recurrent Neural Network and Long Short-Term Memory
Van An Le † Phi Le Nguyen† Yusheng Ji†‡
† Department of Informatics, SOKENDAI (The Graduate University for Advanced Studies)
‡National Institute of Informatics, Tokyo, Japan

## Slide 2: AGENDA
Introduction
Related works
Problem description and goal
Proposed approach
Evaluation
Conclusion and future work

## Slide 3: AGENDA
Introduction
Related works
Problem description and goal
Proposed approach
Evaluation
Conclusion and future work

## Slide 4: Introduction
TRAFFIC MATRIX: an abstract representation of the traffic volume flowing between set of origins and destinations pairs. [1]
Source: ubiquity.acm.org

## Slide 5: Introduction
Traffic Matrix
Network Optimization
Anomaly Detection
Protocol Design
...
QoS provisioning
Traffic matrix plays an important roles in wide range of network management applications/tasks. [1]
Measuring all the traffic network is impractical due to the monitoring resources constraints.
Notes: Không nên để cả câu dài, chỉ viết ý ngắn gọn
Câu thứ 2 để dạng V-ing, thì câu thứ 1 cũng phải để cùng dạng như vậy

## Slide 6: Related works
Network tomography:
Estimating traffic from link data [2].
Infocom
SDN-based traffic aggregation and measurement paradigm [4].
1996
2009
2014
2015
Sigcomm:
Spatial-temporal Compressive sensing approach [3].
Infocom
Adaptive sampling for traffic completion [5].
 | Network tomography based approach
 | Traffic interpolation using Compressive Sensing and Matrix Completion
 | Traffic prediction using Deep Learning approach
Notes: Trong bang tóm tắt góc phải: approach 1 và 3 có chữ approach ở cuối nhưng cái thứ 2 lại không có  nên thống nhất
Trong phần chú thích hình vẽ ở dưới: 4 cái sau đang để format: Tên hội nghị: nội dung bài báo. Nhưng cái thứ nhất thì lại không cùng format đấy.

## Slide 7: Related works
Infocom
Traffic interpolation using tensor completion [6].
2016
Journals:
Traffic Matrix estimation based on deep learning and probabilistic model [7].
2017
Infocom
Traffic recovery under dynamic condition using tensor completion [8].
Infocom
Spatial temporal modelling and prediction in Cellular network using Deep Learning [10].
IEEE Access
Traffic prediction using recurrent convolutional network in Data center [9].
 | Network tomography based approach
 | Traffic interpolation using Compressive Sensing and Matrix Completion
 | Traffic prediction using Deep Learning approach

## Slide 8: Related works
Network Tomography
  Inferring traffic based on link count and routing information
  Under-constrained problem (# of flows >> # of link monitored)
Traffic recovery and interpolation.
  Recovering the missing traffic
  For traffic analysis
Traffic prediction based Deep Learning approach
  Cellular Network and Data center.
  Backbone network?
Notes: Tên của các approach đang không đồng nhất với tên ở trong slide 6
  Traffic prediction based Deep Learning approach: based hay using ?
Mỗi ý nhỏ thứ nhất em định trình bày gì về các approach: techniques ? Ưu điểm ? Hay là gì ? Chị thấy ở 3 approach, mỗi cái trình bày một kiểu  em nên thống nhất format
Mỗi ý nhỏ thứ 2 của em là shortcoming của mỗi approach. Chị nghĩ là nên ghi rõ là cons: …. . Với cả format của các câu em đang không thống nhất. Ví dụ: ở cái approach thứ 2 em chỉ ghi “For traffic analysis”, ở approach thứ 3 em chỉ ghi “Backbone network?  nhìn những phrase này không hiểu rõ được ý em muốn nói gì ?

## Slide 9: Problem description
SDN [11] architecture opens new approaches in comprehensive network monitoring and management.
Monitoring all flows in the network:
  High computational cost
  Traffic overhead
  Impractical
Partial monitoring and PREDICTION
Source: www.ayalpbilisim.com

## Slide 10: AGENDA
Introduction
Related works
Problem description
Proposed approach
Evaluation
Conclusion and future work
Notes: - Trang agenda này phải xuất hiện trước page 9 chứ nhỉ, vì page 9 đã là problem description rồi

## Slide 11: Problem description
Traffic Matrix at time
Traffic Vector
: number of original-destination pairs (OD pairs)
: number of nodes
Flattening

## Slide 12: Problem description
… | … | … | … | …
 | ? | ? |  | ?
… | … | … | … | …
 | ? | ? |  | ?
Timestep
Origin-Destination pairs flows
Prediction model
 | Predicted data
 | Measured data
Time frame

## Slide 13: Semi-recursive prediction
Origin-Destination flows
 | Predicted data
 | Measured data
Consider current timestep
 | Traffic load of flow at time
 | Observed traffic of flow at time
 | Predicted traffic of flow at time
 | Number of history data used for prediction.
 | Binary variable. if traffic of flow at time is measured, otherwise.
 | Number of history data used for prediction.
… | … | … | … | …
 | ? | ? |  | ?
… | … | … | … | …
 | ? | ? |  | ?

## Slide 14: Challenges and Goals
Accumulative error
Direct Prediction
Semi-recursive Prediction
Alleviating the accumulate errors
Correcting the imprecise input data

## Slide 15: Challenges and Goals
Determining the monitored flow set
Designing a scheme for selecting which flow will be monitored in the next timestep.
… | … | … | … | …
? | ? | ? | ? | ?
… | … | … | … | …
? | ? | ? | ? | ?

## Slide 16: AGENDA
Introduction
Related works
Problem description
Proposed approach
Evaluation
Conclusion and future work

## Slide 17: Recurrent Neural Network and Long Short-Term Memory
Source: machinelearning-blog.com

## Slide 18: Traffic prediction using Recurrent Neural Network
LSTM
…
…
…
…
LSTM
LSTM

## Slide 19: Forward and backward networks
LSTM
…
…
LSTM
LSTM
…
LSTM
…
LSTM
LSTM
…
…

## Slide 20: Correcting RNN input
 | Predicted input
 | Measured input
 | Output of forward RNN
 | Output of backward RNN
 | Forward RNN unit
 | Backward RNN unit
 | Predicted input
 | Measured input
 | Output of forward RNN
 | Output of backward RNN
 | Forward RNN unit
 | Backward RNN unit

## Slide 21: Confidence factors
g

## Slide 22: Forward loss and backward loss

## Slide 23
Forward loss and backward loss

## Slide 24: Correcting RNN input
Where:

## Slide 25: Consecutive loss
Time
Original-Destination pairs
 | Predicted data
 | Measured data
: indicates how long has not been monitored
the number of timesteps from when was last monitored till the current timestep
e.g:
… | … | … | … | …
? | ? | ? | ? | ?
… | … | … | … | …
? | ? | ? | ? | ?

## Slide 26: Determining monitored flows
For each , we calculate a “weight” following the equation () and then choosing the lowest flows to measure in the next time step.
Where:
Notes: - Câu “For each , we calculate a “weight” following the equation () and then choosing the lowest flows to measure in the next time step.” nên viết lại thành các phrase ngắn
- Câu “For each 𝑂𝐷_𝑖, we calculate a “weight” 𝑤_𝑖 following the equation () and then choosing the lowest 𝑘 flows to measure in the next time step.” nên viết lại thành các phrase ngắn

## Slide 27: AGENDA
Introduction
Related works
Problem description
Proposed approach
Evaluation
Conclusion and future work

## Slide 28: Abilene dataset
Measurement period: from 2004-03-01 to 2004-09-10
  168 days
Measurement interval: 5 minutes
  288 timestamps per day
Number of nodes: 12
  Number of OD flows: 144
Number of traffic data: 288*168*144 = 6967296

## Slide 29: Experiment setup
Hardware | 
CPU | Intel(R) Core(TM) i7-6800K CPU@3.40GGHz
GPU | GeForce GTX 1080Ti
RAM | 32G
RNN – Configuration | 
Hidden units | 100
Layers | 1
Input dimension | 26
Dropout | 0.2
Training Epoch | 100

## Slide 30: Metrics
Error ratio
Mean absolute errors
Root mean squared errors
is the size of the testing set
Notes: MAE: average absolute errors
RMSE: presents sample standard deviation of the differences between

## Slide 31: Flow prediction result
TRAFFIC PREDICTION OF A RANDOM FLOW

## Slide 32: Performance comparison
48.3%
32.7%
62.9%

## Slide 33: Traffic prediction under consecutive loss
Data of 4 hours (from 10a.m every day) are all loss

## Slide 34: Conclusion
In this work, we have:
Defined the semi-recursive traffic prediction problem
Solved the semi-recursive traffic prediction problem by proposing a novel deep learning model and techniques for correcting the input data and monitored flows determination.
Conducted the preliminary experiments for evaluating our proposed approach.
Notes: “In this work, we have:”  nên bỏ đi
- Câu thứ 2 dài quá, nên viết gọn lại

## Slide 35: Future work
Next, we will:
Examine the relation between the flows in the traffic matrix and capture not only the temporal but also the spatial feature of the traffic matrices.
Design an efficient algorithm for correcting input data and selecting monitored flows.
Notes: - Câu thứ 1 dài quá  nên viết gọn lại

## Slide 36: References
[1] "Recent Advances in Networking", Volume 1, ACM SIGCOMM eBook, August 2013
[2] Vardi, Yehuda. "Network tomography: Estimating source-destination traffic intensities from link data." Journal of the American statistical association 91.433 (1996): 365-377
[3] Zhang, Yin, et al. "Spatio-temporal compressive sensing and internet traffic matrices." ACM SIGCOMM Computer Communication Review. Vol. 39. No. 4. ACM, 2009.
[4] Malboubi, M., Wang, L., Chuah, C. N., & Sharma, P. (2014). Intelligent SDN based traffic (de)Aggregation and Measurement Paradigm (iSTAMP). Proceedings - IEEE INFOCOM, 934–942.
[5] Xie, K., Wang, L., Wang, X., Xie, G., Zhang, G., Xie, D., & Wen, J. (2015). Sequential and adaptive sampling for matrix completion in network monitoring systems. Computer Communications (INFOCOM), 2015 IEEE Conference on, 2443–2451.
[6] Xie, K., Wang, L., Wang, X., Xie, G., Wen, J., & Zhang, G. (2016). Accurate recovery of Internet traffic data: A tensor completion approach. Transaction on Networking, 2016–July, 1–14.
[7] Nie, L., Jiang, D., Guo, L., & Yu, S. (2016). Traffic matrix prediction and estimation based on deep learning in large-scale IP backbone networks. Journal of Network and Computer Applications, 76(October), 16–22.
[8] Xie, Kun, et al. "Accurate recovery of Internet traffic data under dynamic measurements." INFOCOM 2017-IEEE Conference on Computer Communications, IEEE. IEEE, 2017.
[9] Cao, X., Zhong, Y., Zhou, Y., Wang, J., Zhu, C., & Zhang, W. (2017). Interactive temporal recurrent convolution network for traffic prediction in data centers. IEEE Access, 6, 5276–5289.
[10] Wang, J., Tang, J., Xu, Z., Wang, Y., Xue, G., Zhang, X., & Yang, D. (2017). Spatiotemporal modeling and prediction in cellular networks: A big data enabled deep learning approach. IEEE INFOCOM 2017 - IEEE Conference on Computer Communications, 1–9.
[11]

## Slide 37
THANK YOU